## Slide 1: GPGPU-Sim 3.x A Performance Simulator for Many-Core Accelerator Research
Tor M. Aamodt
Wilson W. L. Fung
Tayler Hetherington
University of British Columbia
Version of simulator corresponding to these slides = GPGPU-Sim 3.1.2
Website
gpgpu-sim.org

## Slide 2: Tutorial Goals
Make you more effective in your research using GPGPU-Sim
  Feel free to ask questions when you have them
After this tutorial, you will be able to:
  Describe what GPGPU-Sim simulates
  Setup GPGPU-Sim and run CUDA applications on it
  Do simple performance analysis on CUDA applications with AerialVision
  Extend GPGPU-Sim for your own research

## Slide 3: Quick Survey
How many of you are:
  Graduate students?
  Faculty members?
  Working for government?
  Working for industry?
Have you written a CUDA or OpenCL program before?
Have you used GPGPU-Sim?

## Slide 4: Overview
1 | Brief Background on GPU Computing | 40mins
2 | GPGPU-Sim Overview | 30mins
3 | Demo 1: Setup and Run | 15mins
Coffee Break (10:00 – 10:30am) |  | 
4 | Microarchitecture Timing Model | 85mins
Lunch (12:00 – 1:00pm) |  | 
5a | Software Organization | 25mins
5b | Timing Model (Software) | 50mins
5c | Power Model - GPUWattch | 45mins
Coffee Break (3:00 – 3:30pm) |  | 
6 | The GPU Design Space | 10mins
7a | Demo 2: Debugging Tool | 15mins
7b | Demo 3: Visualizing Performance | 30mins
8 | Extending GPGPU-Sim (with GPUWattch) | 30mins
9 | Wrap Up and Discussion | 15mins

## Slide 5: What is a GPU?
GPU = Graphics Processing Unit
  Optimized for Highly Parallel Workloads
  Highly Programmable
  Commodity Hardware (“Desktop Supercomputing”)
Nvidia’s GTX580: 16 x 32-wide multiprocessors
  512 ALUs
24,576 concurrent threads

## Slide 6: GPU Computing
  4 core CPU + 1536 core GPU
  Heterogeneous computing

## Slide 7: Why GPU?
*Slide from GTC 2011, GPU Computing: Past, Present and Future, David Luebke, NVIDIA

## Slide 8: Why GPU?
*Slide from GTC 2011, GPU Computing: Past, Present and Future, David Luebke, NVIDIA

## Slide 9: Why GPU?
*Slide from AFDS 2011, The Programmer’s Guide to the APU Galaxy, Phil Rogers, AMD

## Slide 10: Why GPU?
OpenCL supported GPUs (besides AMD and NVIDIA)
  AdrenoTM 3xx GPU from Qualcomm
  MaliTM-T600 Series GPUs from ARM
  HD 4000 on Intel’s Ivy Bridge
  Intel Xeon Phi (Knights Corner)
GPU Computing is gaining broad industry support.

## Slide 11: Programming Model
Traditional viewpoint
  CPU offload data parallel code sections onto the GPU
Correct viewpoint? (if you want 100x speedup)
  GPU = computation workhorse
  CPU = sequential code “accelerator” and I/O offload engine

## Slide 12: GPU Microarchitecture Overview (10,000 feet)
Single-Instruction, Multiple-Threads
GPU
Interconnection Network
SIMT Core Cluster
SIMT
Core
SIMT
Core
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Off-chip DRAM
SIMT Core Cluster
SIMT
Core
SIMT
Core
SIMT Core Cluster
SIMT
Core
SIMT
Core

## Slide 13: CUDA and OpenCL
Extensions of C to support coprocessor model
GPGPU-Sim support both
  This tutorial focus on CUDA
    More applications today
Notes: Next few slides:
Brief introduction to CUDA programming model
Why? GPU microarchitecture is designed for CUDA programs.
The programming model has driven design decisions in GPGPU-Sim.

## Slide 14: CUDA Thread Hierarchy
Kernel Launch = Grid of Blocks of Threads
Threads are scalar threads
Source: CUDA programming manual

## Slide 15: CUDA Memory Model
Memory Spaces
  Shared
  Global
  Local
  Constant
  Texture
Source: CUDA programming manual

## Slide 16: SIMT Execution Model
Programmers sees MIMD threads (scalar)
GPU HW bundles threads into warps and runs them in lockstep on SIMD hardware
A: v = foo[tid.x];
B: if (v < 10)
C: v = 0;
else
D: v = 10;
E: w = bar[tid.x]+v;
Time
A
T1
T2
T3
T4
B
T1
T2
T3
T4
C
T1
T2
D
T3
T4
E
T1
T2
T3
T4
foo[] = {4,8,12,16};
Notes: MIMD = multiple-instruction, multiple-data

## Slide 17: CUDA Syntax Highlights
Declaration specifiers to indicate where things live
  __global__ void foo(...); // runs on GPU, callable from CPU
  __device__ void bar(...); // function callable from a GPU thread
Parallel kernel launch
  foo<<<500, 128>>>(...); // 500 blocks, 128 threads each
Special variables for thread identification in kernels
  dim3 threadIdx; dim3 blockIdx; dim3 blockDim;

## Slide 18: CUDA Example Code
Standard C Code
void saxpy_serial(int n, float a, float *x, float *y)
{
for (int i = 0; i < n; ++i)y[i] = a*x[i] + y[i];
}
// Invoke serial SAXPY kernel
saxpy_serial(n, 2.0, x, y);
CUDA code
__global__ void saxpy_parallel(int n, float a, float *x, float *y)
{
int i = blockIdx.x*blockDim.x + threadIdx.x;
if(i<n)
y[i]=a*x[i]+y[i];
}
main() {
… // omitted: allocate and initialize memory
// Invoke parallel SAXPY kernel with 256 threads/block
int nblocks = (n + 255) / 256;
saxpy_parallel<<<nblocks, 256>>>(n, 2.0, x, y);
… // omitted: transfer results from GPU to CPU
}
High performance computing with CUDA, SC09 Tutorial, David Luebke, NVIDIA
Notes: saxpy = single precision ax + y

## Slide 19: GPGPU-Sim in a Nutshell
Microarchitecture performance model of contemporary GPUs
  New: Power Model: GPUWattch
Runs unmodified CUDA/OpenCL
BSD License
Focus of this tutorial: GPGPU-Sim version 3.1.2 and later

## Slide 20: GPGPU-Sim 3.1.2
Since GPGPU-Sim 2.1.1b:
  Refactored for C++ Object-Oriented Implementation
  Redesigned Timing Models
    SIMT Core model, Cache models, GDDR5 timing … (later)
  Asynchronous Kernel Calls
  Concurrent Kernel Execution
  Support for CUDA 3.1
Since GPGPU-Sim 3.0.1:
  Updated timing model to model Fermi more accurately
  Much more robust SASS support
  Support for CUDA 4.0 and later; OpenCL with newer drivers
  Power Model: GPUWattch

## Slide 21: Accuracy
Chart: RODINIA Benchmark Suite Quadro FX5800 SASS GPGPU-Sim 3.1.0 – Correlation: 98.37%
Similarity Score
copyChunks_kernel()
Back Propagation
bpnn_layerforward_CUDA()
HotSpot
calculate_temp()

## Slide 22: Accuracy
Chart: RODINIA Benchmark Suite Tesla C2050 (Fermi) SASS GPGPU-Sim 3.1.0 – Correlation: 97.35%
Notes: Outliers:
BackPropagation – bpnn_layerforward_CUDA (Too Slow)
BackPropagation – bpnn_adjust_weights_cuda (Too Slow)
HotSpot– last calculate_temp (Too Fast)
HeartWall – kernel (Too Slow)
SingularSimilarity – copyChunks_kernel (Too Fast)

## Slide 23: Accuracy (Average Power)
Chart: NVIDIA GTX 480

## Slide 24: Dependencies
Linux
CUDA Toolkit (3.1 / 4.0 / 4.2)
Standard Development Environment
  GCC, Make, etc.
No GPU Hardware for CUDA
Notes: Optional: For OpenCL only
- CUDA capable GPU Hardware (Local/Remote)

## Slide 25: Citation
If you use GPGPU-Sim (either 2.x or 3.x) in your publication, please cite our ISPASS 2009 paper:
Please indicate which version of GPGPU-Sim you used / extended
  E.g. “GPGPU-Sim version 3.1.2”
  Ali Bakhoda, George L. Yuan, Wilson W. L. Fung, Henry Wong, Tor M. Aamodt, Analyzing CUDA Workloads Using a Detailed GPU Simulator, In proceedings of the IEEE International Symposium on Performance Analysis of Systems and Software (ISPASS), pp. 163-174, Boston, MA, April 26-28, 2009.

## Slide 26: Session Summary
GPU Computing
CUDA Programming Model Concepts
  Thread Hierarchy
  Memory Spaces
  SIMT Execution Model
GPGPU-Sim: Timing + power simulator of modern GPUs
  Good accuracy
  Runs on systems without HW GPUs

## Slide 27: Overview
1 | Brief Background on GPU Computing | 40mins
2 | GPGPU-Sim Overview | 30mins
3 | Demo 1: Setup and Run | 15mins
Coffee Break (10:00 – 10:30am) |  | 
4 | Microarchitecture Timing Model | 85mins
Lunch (12:00 – 1:00pm) |  | 
5a | Software Organization | 25mins
5b | Timing Model (Software) | 50mins
5c | Power Model: GPUWattch | 45mins
Coffee Break (3:00 – 3:30pm) |  | 
6 | The GPU Design Space | 10mins
7a | Demo 2: Debugging Tool | 15mins
7b | Demo 3: Visualizing Performance | 30mins
8 | Extending GPGPU-Sim (with GPUWattch) | 30mins
9 | Wrap Up and Discussion | 15mins