## Slide 1: Overview
1 | Brief Background on GPU Computing | 40mins
2 | GPGPU-Sim Overview | 30mins
3 | Demo 1: Setup and Run | 15mins
Coffee Break (10:00 – 10:30am) |  | 
4 | Microarchitecture Timing Model | 85mins
Lunch (12:00 – 1:00pm) |  | 
5a | Software Organization | 25mins
5b | Timing Model (Software) | 50mins
5c | Power Model: GPUWattch | 45mins
Coffee Break (3:00 – 3:30pm) |  | 
6 | The GPU Design Space | 10mins
7a | Demo 2: Debugging Tool | 15mins
7b | Demo 3: Visualizing Performance | 30mins
8 | Extending GPGPU-Sim (with GPUWattch) | 30mins
9 | Wrap Up and Discussion | 15mins

## Slide 2: Software Organization Overview
Introduce GPGPU-Sim modules
Functional Simulation
  Interfacing with CUDA and OpenCL
  Details of PTX simulation
Timing Model
Power Model: GPUWattch
5 Min Break
5 Min Break

## Slide 3: Why should you learn about functional simulation?
GPGPU-Sim already runs many existing GPU workloads:
  ISPASS 2009
  RODINIA
  CUDA SDK
We implement features on a demand basis:
  When they are needed by an application that we are interested in studying
  If you find something missing, then add it!

## Slide 4: Why should you learn about functional simulation?
As researchers, we are interested in enhancing GPUs for future workloads.
  Some of them will not work on GPGPU-Sim out-of-the-box.
At some point, you will need to extend the function simulator in GPGPU-Sim to run your research workloads.

## Slide 5: Our Own Experience
Thread Block Compaction (HPCA 2011)
  Implemented low-level CUDA API for ray-tracing workload
  Allow GPU to access CPU memory space directly for VisBench
Hardware Transactional Memory for GPU Architectures (MICRO 2011)
  Extended functional simulator to support transactions

## Slide 6: Session Objectives
After this session, you will be able to:
  Extend GPGPU-Sim to get your workload running on it for your research
    Implement new instructions
    Update behavior for existing instructions
    Fill in unimplemented parts of CUDA/OpenCL API
  Evaluate your research microarchitectures on GPGPU-Sim
    Implement your research idea in the timing model

## Slide 7: Modules Overview
CUDA/OpenCL API library interface
PTX instruction set emulator
Timing model
Power model
CUDA/OpenCL
API Library
Interface
PTX Emulator
(CUDA-Sim)
GPGPU-Sim
Entrypoint
Timing
Model
Abstract
HW Model
Power
Model: GPUWattch
Notes: 7

## Slide 8: Interface to CUDA/OpenCL
API Interface
How GPGPU-Sim starts
PTX Loading / Parsing
Stream Manager

## Slide 9: Interface to CUDA/OpenCL
CUDA and OpenCL applications:
  Include code that runs on the host (CPU)
  Use an API to communicate with GPU
  API is defined in various header files
  Implementation in DLL
GPGPU-Sim:
  Runs host code on CPU
  Functionally emulates API
  I.e., if you run GPGPU-Sim on a Core 2 Duo machine, the host code runs natively on your Core 2 Duo processor (is not simulated as part of timing model)

## Slide 10: Interface to CUDA/OpenCL API
We implement versions of OpenCL / CUDA interface calls in a new DLL.
Adjust LD_LIBRARY_PATH and CUDA/OpenCL application runs on simulator rather than GPU hardware.
Given our research focus, we have implemented only what was required to get applications we were interested in running.
CUDA
Application
CUDA
Runtime Library
libcudart.so
GPGPU-Sim

## Slide 11: Interface to CUDA API
Example of interface code between host and simulator. This is the code that actually starts running the functional and timing models. Call to cudaLaunch is generated by nvcc from “<<<>>>” notation.
__host__ cudaError_t CUDARTAPI cudaLaunch( const char *hostFun )
{
CUctx_st* context = GPGPUSim_Context();
char *mode = getenv("PTX_SIM_MODE_FUNC");
if( mode )
sscanf(mode,"%u", &g_ptx_sim_mode);
gpgpusim_ptx_assert( !g_cuda_launch_stack.empty(), "empty launch stack" );
kernel_config config = g_cuda_launch_stack.back();
struct CUstream_st *stream = config.get_stream();
printf("\nGPGPU-Sim PTX: cudaLaunch for 0x%p (mode=%s) on stream %u\n", ... );
kernel_info_t *grid = gpgpu_cuda_ptx_sim_init_grid(hostFun,config.get_args(),
config.grid_dim(),
config.block_dim(),context);
std::string kname = grid->name();
dim3 gridDim = config.grid_dim();
dim3 blockDim = config.block_dim();
printf("GPGPU-Sim PTX: pushing kernel \'%s\' to stream %u, ... );
stream_operation op(grid,g_ptx_sim_mode,stream);
g_stream_manager->push(op);
g_cuda_launch_stack.pop_back();
return g_last_cudaError = cudaSuccess;
}

## Slide 12: GPGPU-Sim Startup Details
Some CUDA code called before main() during initialization of global variables. __cudaRegisterFunction, __cudaRegisterVar These provide information about device code (and how to call it).
First call to any CUDA API function triggers simulator initialization (gpgpu_ptx_sim_init_perf()).
  Read environment variables (debug info, sim mode)
  Parse option files
  Initialize GPU uArch Model, Stream Manager
First call to __cudaRegisterFatBinary()
  Load/parse PTX kernels, determine post-dominators

## Slide 13: Loading PTX
CUDA 3.1: Fatbin
  Overload __cudaRegisterFatBinary() to extract PTX from executable
CUDA 4.0 and later: cuobjdump
  Call cuobjdump to obtain PTX/SASS
  Executable must be compiled with CUDA 4.0 or later
Multiple versions of kernel PTX
  Default: Use PTX with highest SM version

## Slide 14: PTX Parsing, Post-Dominator Detection
GPGPU-Sim has a flex+bison parser to read in PTX
  Default: Read PTX text embedded within binary
Same parser is used for SASS (PTXPlus)
Why flex+bison? Flexibility.
  When NVIDIA update their PTX syntax, we can update our parser accordingly.
Post-dominators
  Handle warp divergence in simulation
  Determined with standard control flow analysis

## Slide 15: Parsing PTX
Next two slides illustrate snippets of code from lexer and parser

## Slide 16: cuda-sim/ptx.l – find tokens
abs TC; ptx_lval.int_value = ABS_OP; return OPCODE;
add TC; ptx_lval.int_value = ADD_OP; return OPCODE;
and TC; ptx_lval.int_value = AND_OP; return OPCODE;
…
\.align TC; return ALIGN_DIRECTIVE;
\.byte TC; return BYTE_DIRECTIVE;
\.const\[[0-9]+\] TC; return CONST_DIRECTIVE;
…
"%tid" TC; ptx_lval.int_value = TID_ID; return SPECIAL_REGISTER;
…
\.u32 TC; return U32_TYPE;
\.u64 TC; return U64_TYPE;
\.f16 TC; return F16_TYPE;
\.f32 TC; return F32_TYPE;
…
\.equ TC; return EQU_OPTION;
\.neu TC; return NEU_OPTION;
\.ltu TC; return LTU_OPTION;
…
"]" TC; return RIGHT_SQUARE_BRACKET;
"<" TC; return LEFT_ANGLE_BRACKET;
">" TC; return RIGHT_ANGLE_BRACKET;
"(" TC; return LEFT_PAREN;
…

## Slide 17: cuda-sim/ptx.y – read instructions
…
%token <string_value> STRING
%token <int_value> OPCODE
%token ALIGN_DIRECTIVE
%token BYTE_DIRECTIVE
…
%%
input: /* empty */
| input directive_statement
| input function_defn
| input function_decl
;
…
instruction: opcode_spec LEFT_PAREN operand RIGHT_PAREN { set_return(); } COMMA operand COMMA LEFT_PAREN operand_list RIGHT_PAREN
| opcode_spec operand COMMA LEFT_PAREN operand_list RIGHT_PAREN
| opcode_spec operand_list
| opcode_spec
;
…

## Slide 18: Stream Manager + Abstract GPU
GPGPU-Sim Thread
  gpgpu_sim_thread_concurrent()
  do {
  Wait for streamOp;
  do {
  Obtain streamOp;
  Perform streamOp;
  gpu->cycle();
  active = gpu->active() or
  streamMgr->empty();
  if (gpu->finished_kernel())
  gpu->print_stats();
  } while (active);
  } while (!gpu_done);
Kernel
Launch
CUDA
Memcpy
Sync
GPGPU-Sim Thread
Host CPU
CUDA
API
Stream 0

## Slide 19: Functional Simulator
Key Objects in Module
Three main aspects
  How are threads simulated?
  How are instructions simulated?
  How are values communicated between threads?
Memory Space Buffer
Pure Functional Simulator

## Slide 20: Inside Functional Simulation: Key Objects
core_t
function_info
ptx_instruction
ptx_instruction
ptx_instruction
PC(0x0)
PC(0x8)
PC(0x10)
Control Flow
Analysis
Symbol Table
kernel_info
Param Memory
Grid/Block Dim
Launch Status
Global Memory
ptx_cta_info
Shared Memory
Barrier
gpgpu_t
GPU Memory
Management
ptx_thread_info
ptx_thread_info
ptx_thread_info
Local Memory
Thread IDs
Registers
Program Counters
Call stack
SIMT Stacks

## Slide 21: How are threads simulated (functionally)?
Thread = program counter +
set of registers +
set of local memory locations
CTA (block) = set of threads with access to a shared memory + barrier
New in GPGPU-Sim 3.x: Expose notion of “warp” in functional simulator
Support undocumented barrier behavior
Notes: Subtle consequence of exposing warp in functional simulator:
- Has to support for warp divergence as well

## Slide 22: How are instructions simulated (functionally)?
Code for simulating instructions in cuda-sim/instruction.cc
  1:1 mapping opcode  implementation function
  Mapping in opcode.def
Threads initialized during launching of blocks.
Functional execution at issue stage of timing pipeline:
  Calls ptx_thread_info::ptx_exec_inst()
  Inside: “giant switch statement” simulation approach (emulation)
Lookup instruction “object” corresponding to program counter
  PTX: Assume 8-byte per instruction

## Slide 23: How are values communicated between threads?
Threads can communicate through
  Global memory
  Shared memory
We simulate all instructions as they reach issue stage of pipeline
  This includes loads and stores that access memory.
  Except for atomics: We simulate them functionally once atomic operation exits the memory partition in timing model.
    atom_impl() calculates effective memory address and setups callback function
Most CUDA code avoids intra-kernel communication through global memory
  Relaxed memory ordering

## Slide 24: Memory Space Buffer
Functionally implements various memory spaces
  Map of memory address  pages
  Each memory space buffer may contain infinite # pages
Global, texture, constant memory spaces share the same buffer
Each block has a shared memory buffer
Each thread has a local memory buffer
Implementation in cuda-sim/memory.[h,cc]

## Slide 25: Pure Functional Simulator
Great for:
  Profiling application behavior
  Prototyping new instructions
Recreated in GPGPU-Sim v3.1.0
Mostly contained in a single class: functionalCoreSim
Execute one thread block at a time
  Execute warps in round-robin

## Slide 26: Overview
1 | Brief Background on GPU Computing | 40mins
2 | GPGPU-Sim Overview | 30mins
3 | Demo 1: Setup and Run | 15mins
Coffee Break (10:00 – 10:30am) |  | 
4 | Microarchitecture Timing Model | 85mins
Lunch (12:00 – 1:00pm) |  | 
5a | Software Organization | 25mins
5b | Timing Model (Software) | 50mins
5c | Power Model: GPUWattch | 45mins
Coffee Break (3:00 – 3:30pm) |  | 
6 | The GPU Design Space | 10mins
7a | Demo 2: Debugging Tool | 15mins
7b | Demo 3: Visualizing Performance | 30mins
8 | Extending GPGPU-Sim (with GPUWattch) | 30mins
9 | Wrap Up and Discussion | 15mins

## Slide 27: Software Organization Overview
Introduce GPGPU-Sim modules
Interfacing with CUDA and OpenCL
Details of PTX simulation
Timing Model
Power Model: GPUWattch

## Slide 28: Abstract HW Model
Interface between functional simulation and timing simulation
core_t
shader_core_ctx
ptx_instruction_t
warp_inst_t
inst_t
gpgpu_t
gpgpu_sim
Abstract Model
Timing Model

## Slide 29: Microarchitecture Model (Revisitied)
GPU
Interconnection Network
SIMT Core Cluster
SIMT
Core
SIMT
Core
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Off-chip DRAM
SIMT Core Cluster
SIMT
Core
SIMT
Core
SIMT Core Cluster
SIMT
Core
SIMT
Core

## Slide 30: Timing Model (Software Overview)
memory_partition_unit
GDDR3/GDDR5
gpgpu_sim
simt_core_cluster
shader_core_ctx
shader_core_ctx
memory_partition_unit
GDDR3/GDDR5
Off-chip DRAM
simt_core_cluster
shader_core_ctx
shader_core_ctx
simt_core_cluster
shader_core_ctx
shader_core_ctx
memory_partition_unit
GDDR3/GDDR5
Interconnection Network (intersim)

## Slide 31: Timing Model: gpgpu_sim
Top Level Object
A virtual GPU with timing model
  Contains all components for timing simulation
Specific responsibilities:
  Initialization
  Kernel Launch
  Clock Domain
  Main Simulation Loop
Implemented in gpgpu-sim/gpu-sim.[h,cc]

## Slide 32: Timing Model: Initialization
gpgpu_sim::gpgpu_sim()
  Allocate and initialize microarchitecture model and statistic collection structures
  Called in gpgpu_ptx_sim_init_perf()
    At the first CUDA API call
  Only one global instance: g_the_gpu

## Slide 33: Timing Model: Main Simulation Loop
do {
Wait for streamOp;
do {
Obtain streamOp;
if (streamOp == Launch)
gpu->launch();
gpu->cycle();
active = gpu->active() or
streamMgr->empty();
if (gpu->finished_kernel())
gpu->print_stats();
} while (active);
} while (!gpu_done);
General Stats Log
Probe GPU Activity:
Running a kernel
Accessing memory
Simulate a cycle
in GPU
Push a kernel into
GPU launch queue
Notes: Recall the GPGPU-Sim thread we showed you earlier? Here is now the gpgpu_sim class interfaces with it.

## Slide 34: Timing Model: Main Simulation Loop
Inside gpgpu_sim::cycle():
  Check all clock domains
    if (clock_mask & CORE) { … }
  Execute the ones that are ready
  Currently, 4 domains:
    CORE – SIMT Core + Thread Block Issue
    ICNT – Interconnection Network
    DRAM – DRAM + Request Scheduler
    L2 – L2 Cache in Memory Partition

## Slide 35: Timing Model: Thread Block Issue
gpgpu_sim::issue_block2core():
  Issue new thread blocks to core
    Limit calculated with shader_core_config::max_cta()
  Initializes the threads inside the new blocks
    Calls interface to functional model: ptx_sim_init_thread()
  Hierarchical Block Distribution
    Top Level  SIMT Core Clusters  SIMT Cores
Cluster 0
B0
B3
B6
Cluster 1
B1
B4
Cluster 2
B2
B5
SC 0
SC 1
SC 2
SC 3
SC 4
SC 5

## Slide 36: Timing Model: simt_core_cluster
Collection of SIMT cores
  core_cycle(): simulation a cycle in each core
Interface them with interconnect
icnt_cycle()
icnt_inject_request_packet()
shader_memory_interface

## Slide 37: Timing Model: SIMT Core
Class shader_core_ctx in gpgpu-sim/shader.[h,cc]
  Derived from core_t
  Contains the state of a SIMT Core
Major components in separate classes
  scheduler_unit
  scoreboard
  opndcoll_rfu_t (Operand Collector)
  simd_function_unit
  ldst_unit (Memory Unit)

## Slide 38: Timing Model: SIMT Core
shader_core_ctx::cycle()
ALU
ALU
ALU
I-Cache
Decode
I-Buffer
Score
Board
Issue
Operand
Collector
MEM
ALU
Fetch
SIMT-Stack
Done (WID)
Valid[1:N]
Branch Target PC
Pred.
Active
Mask
fetch()
decode()
issue()
read_operand()
execute()
writeback()
Call Order (Order of Stall Propagation)
Notes: The components are organized into stages.
The reverse order calling is a classic trick used by other cycle-level simulators as well.

## Slide 39: Timing Model: Pipeline Connection
ALU
ALU
ALU
I-Cache
Decode
I-Buffer
Score
Board
Issue
Operand
Collector
MEM
ALU
Fetch
SIMT-Stack
Done (WID)
Valid[1:N]
Branch Target PC
Pred.
Active
Mask
warp_inst_t
(grouped in register_set)
ifetch_buffer_t
shd_warp_t
Timing state of a warp
I-Buffer Entry for each warp
warp_inst_t
v
shd_warp_t
Timing state of a warp
I-Buffer Entry for each warp
warp_inst_t
v
shd_warp_t
Timing state of a warp
I-Buffer Entries for warp
warp_inst_t
v
ptx_thread_info
ptx_thread_info
ptx_thread_info
ptx_thread_info
ptx_thread_info
SIMT Stack
SIMT Stack
SIMT Stack
core_t

## Slide 40: Timing Model: Warp Instruction
warp_inst_t
A dynamic “SIMD” instruction executed by a warp
Pipeline Register
Implements access coalescing logic
  Groups individual accesses from threads into wider/bank-conflict-free accesses
  Per-thread info  mem_access_t
  See warp_inst_t::generate_mem_accesses()
inst_t
Static Info
warp_inst_t
active mask
per_thread_info
  dram_callback_t
access_q
ptx_instruction
Func Exec

## Slide 41: Timing Model: Memory Access
mem_access_t
Coalesced memory access from a warp
Consumed in ldst_unit
mem_fetch
Memory request structure that is passed to the cache model and modules in the memory sub-system.
Has a copy of the warp_inst_t + mem_access_t that created the request
  No need for tracker inside SIMT Core
  Access to atom_callback via warp_inst_t
Generated in ldst_unit::cycle()
Destroyed in ldst_unit::writeback() for reads and inside memory_partition_unit for writes
SIMT Core
Memory Subsystem:
Interconnect
L2
DRAM
Mem Unit
Writeback
mem_fetch
Cache
mem_fetch
mem_fetch
warp_inst_t
mem_access_t

## Slide 42: Timing Model: Fetch Stage
Checks for warps that completed execution
  Release resource
Selected a warp via m_last_warp_fetched and access I-cache
  Hit: Send to decode stage
  Miss: Send instruction fetch request off core, try again after I-cache is filled

## Slide 43: Timing Model: Decode Stage
Obtain instruction (warp_inst_t) from functional simulator
  Calls ptx_fetch_inst(pc)
Push into I-Buffer of the corresponding warp
  Calls shd_warp_t::ibuffer_fill()
  Can push up to 2 instructions per-cycle
Notes: ptx_fetch_inst(pc) returns a pointer to ptx_instruction. which is cast into warp_inst_t*.

## Slide 44: Timing Model: Issue Stage
Calls scheduler_unit::cycle() for every instance of scheduler_unit
Calls shader_core_ctx::issue_warp() for each warp selected by the scheduler unit
  Perform functional execution: Calls func_exec_inst()  execute_warp_inst_t()
  Coalesce memory accesses and push them into m_access_q in warp_inst_t: Calls warp_inst_t::generate_mem_accesses()
  Update SIMT Stack for warp
  Lock output register(s) in scoreboard
  Send instruction to operand collector

## Slide 45: Timing Model: Scheduler Unit
scheduler_unit in gpgpu-sim/shader.[h,cc]
  add_supervised_warp_id()
  cycle()
Scheduler for a subset of warps
  Model dual scheduler in Fermi
Warp can be issued if:
  Valid instruction in I-Buffer
  Instruction does not read/write locked register (Scoreboard)
  Execution unit is available
W0
W1
W2
W3
W4
W6
...
...
Sched 0
Sched 1
Operand Collector

## Slide 46: Timing Model: Scoreboard
Scoreboard in gpgpu-sim/scoreboard.[h,cc]
reserveRegister(): Lock register for instruction
releaseRegister(): Unlock register
checkCollision(): Check if instruction accesses any locked register

## Slide 47: Timing Model: SIMT Stack
simt_stack in abstraction_model.[h,cc]
  launch()
  get_active_mask()
  update()
Interaction with shader_core_ctx only in issue():
In scheduler_unit::cycle()
  Calls get_active_mask()
In shader_core_ctx::issue_warp()  core_t::updateSIMTStack()
  Calls update() after functional execution

## Slide 48: Timing Model: Register Read Stage
Scheduler Units
m_dispatch_port
[ID_OC_SP]
m_issue_port
[OC_EX_SP]
Operand Collector
(opndcoll_rfu_t m_operand_collector)
m_sp_unit
Scheduler Units
m_dispatch_port
[ID_OC_SFU]
m_issue_port
[OC_EX_SFU]
m_sfu_unit
m_dispatch_port
[ID_OC_MEM]
m_issue_port
[OC_EX_MEM]
m_ldst_unit

## Slide 49: Timing Model: Operand Collector
opndcoll_rfu_t in gpgpu-sim/shader.[h,cc]
Set of subclasses
Name | Description
arbiter_t | Arbitrate accesses to the register file banks
op_t | A read/write to a single register
allocation_t | Link op_t to an allocated access in arbiter_t
input_port_t | Input to operand collector
collector_unit_t | Collector Unit - One for each warp instruction
dispatch_unit_t | Dispatch a warp instruction with all operands fetched to the corresponding unit

## Slide 50: Timing Model: Operand Collector
opndcoll_rfu_t::step()  Cycle function
For each input port, allocate_cu()
  Allocate a free collector unit for the warp instruction
  Push its register reads into queues in the arbiter unit
allocate_reads()
  Process reads that have no bank conflict
dispatch_ready_cu()
  Each dispatch unit selects a collector unit with fetched operands
  Sends its instruction to output port
opndcoll_rfu_t::writeback()
  Allocate bank for writes to registers (has priority over reads)

## Slide 51: Timing Model: Execution Stage
Calls cycle() for every functional unit
  ALU Units (SP, SFU)
  Memory Unit
Implements a result bus reservation system for groups of ALU units that shares a common writeback bus
  Prevent stalling inside the units

## Slide 52: Timing Model: ALU Pipeline
pipelined_simd_unit
SP unit and SFU unit
Instruction-dependent BW and Latency

## Slide 53: Timing Model: Memory Unit
ldst_unit
Instantiates and operates on all in-core memories
  Texture cache: m_L1T
  Constant cache: m_L1C
  Data cache: m_L1D
  Shared memory: m_pipeline_reg
Off-core interface: m_icnt
Mem_fetch allocator: m_mf_allocator
Operates at a clock_multipler() rate
  Model half-warps

## Slide 54: Timing Model: Memory Unit
ldst_unit::cycle()
Process memory responses from m_response_fifo
Service instruction at m_dispatch_reg
  One access (mem_access_t) / cycle
  Stall until every access in instruction’s m_access_q is processed
  shared_cycle()
  constant_cycle()
  texture_cycle()
  memory_cycle()
ldst_unit::writeback()
Writeback for one of the component (client)
  Optional: Fill caches
  Writeback data to register via operand collector
  Signal scoreboard to unlock register(s)
process_memory_access_queue()
Access cache
m_dispatch_reg
m_access_q:
mem_access_t
mem_access_t
mem_access_t

## Slide 55: Timing Model: Cache Models
See gpgpu-sim/gpu-cache.[h,cc]
Common Components:
tag_array: Cache Line States, Replacement
mshr_table: Queues of Pending Requests
No data array – Data is stored in functional simulator
Hierarchy of Models:
cache_t: General Interface
baseline_cache: Non-blocking cache with request served out-of-order
read_only_cache: Read accesses only
data_cache: Allow read and write accesses
l1_cache and l2_cache: Different Policies
texture_cache: Read accesses in FIFO
Each instance has a reference to a memory interface (m_memport) for cache requests/writebacks

## Slide 56: Timing Model: Cache Models
Common interface:
access(mem_fetch *mf)
  Probe the tag_array (no state change)
  New: Call event handler according to policy
    Read Hit
    Read Miss
    Write Hit
    Write Miss
cycle()
  Move mem_fetch from m_miss_queue to m_memport
fill()
  Update cache block status
  Mark entry in mshr_table as ready

## Slide 57: Timing Model: Cache Models
Handler | Action
rd_hit_base | Access the tag_array (Update LRU stack, line state)
rd_miss_base | Try to allocate resource to handle miss A cache line for replacement Entry in mshr_table Entry in m_miss_queue Fail to allocate  Return Resource Failure
wr_hit_wb | Mark line as modified
wr_hit_wt | Mark line as modified + Send write request
wr_hit_we | Evict line + Send write_request
wr_hit_global_we_local_wb | Global Memory Space: wr_hit_we Local Memory Space: wr_hit_wb
wr_miss_wa | Read missed line into cache + Mark line as modified
wr_miss_nowa | No Write-Allocate: Send write request

## Slide 58: Timing Model: Interfaces
SIMT Core
  mem_fetch_interface: Generic interface used by cache models
    full(unsigned int size, bool write)
    push(mem_fetch *mf)
  shader_memory_interface: To SIMT Core Cluster/Interconnection Network
  perfect_memory_interface: Direct loop back to model zero latency + infinite bandwidth

## Slide 59: Timing Model: Interfaces
Interconnection Network:
  icnt_has_buffer(): Check for input buffer space
  icnt_push(): Push packet into network
  icnt_pop(): Pop packet from network
  icnt_transfer(): Run network for a cycle

## Slide 60: Timing Model: Interfaces
Memory Partition (L2 + DRAM):
  full(): Queues in memory partition full?
  push(): Push request into memory partition
  pop(): Obtain info for completed request
  top(): Pop completed request
mem_req = m_mem_partition[x]->top();
if (icnt_has_buffer(mem_req.info)) {
icnt_push(mem_req);
m_mem_partition[x]->pop();
}
Flow Control

## Slide 61: Timing Model: Memory Partition
memory_partition_unit in gpgpu_sim/l2cache.[h,cc]
Interconnection Network
Memory Partition
L2
Cache
Bank
DRAM
Access
Scheduler
Off-Chip DRAM Channel
DRAM
Timing
Model
Atomic
Operation
Execution
ROP Queue
ICNTL2 Queue
L2DRAM Queue
DRAM Latency Queue
DRAML2 Queue
L2ICNT Queue

## Slide 62: Timing Model: Memory Partition
Memory Partition
m_L2cache
m_dram
Off-Chip DRAM Channel
m_dram
Atomic
Operation
Execution
m_rop
m_icnt_L2_queue
m_L2_dram_queue
m_dram_latency
_queue
m_dram_L2_queue
m_L2_icnt_queue
full()
push()
top()
pop()
cache_cycle()
dram_cycle()

## Slide 63: Timing Model: Memory Partition
L2 Cache = data_cache
  The same model for L1
Atomic operation executed in pop()
  Calls mem_fetch::do_atomic()
  Calls atom_callback() for each thread
DRAM Access Schedule + Timing = dram_t

## Slide 64: Timing Model: Memory Partition
Flow Control:
Queues = fifo_pipeline
  Limited Capacity: Model flow control (bandwidth)
ROP Queue and DRAM Latency Queue
  Model empty pipe latency
  At Push: Obtain ready_cycle = current_cycle + min_latency
  At Pop: Wait until current_cycle == ready_cycle
ROP Queue
ICNTL2 Queue
full() checks this
push() into this

## Slide 65: Timing Model: DRAM Model
DRAM Scheduler: frfcfs_scheduler in dram_sche.[h/cc]
  Models a First-Ready-First-Come-First-Serve Access Scheduler (Rixner et al.)
DRAM Timing Model: dram_t in dram.[h/cc]
  Models the DRAM access timing
    Detail GDDR3/GDDR5 spec
  Contains a FIFO scheduler

## Slide 66: Timing Model: DRAM Model
Modeling Detail GDDR3/GDDR5 Timing:
Set of Constraints  Counters
Each action has a set of constraints
  Delay action until all constraints met (i.e. all corresponding counters == 0)
  Action creates new constraints for other actions (i.e. reset counters to timing parameter)
All counters are decremented every cycle

## Slide 67: Timing Model: DRAM Model
...
if (RRDc == 0 and
bank[j]->state == BANK_IDLE and
bank[j]->RPc == 0 and
bank[j]->RCc == 0)
{
Activate Row for bank[j];
RRDc = m_config->tRRD;
bank[j]->RCDc = m_config->tRCD;
bank[j]->RASc = m_config->tRAS;
bank[j]->RCc = m_config->tRC;
}
...
if (RRDc > 0) RRDc--;
if (bank[j]->RCDc > 0) bank[j]->RCDc--;
...
Check
Timing
Constraint
Update
Timing
Constraint
Inside dram_t::cycle()
Decrement Counters

## Slide 68: Configuration Organization
Each major module has its own configuration structure
  Hooked up to the global option parser
gpgpu_sim
gpgpu_sim_config
shader_core_ctx
shader_core_config
memory_partition
memory_config
gpgpu_t
gpgpu_functional_sim_config

## Slide 69: Adding Configuration Options
Use option_parser module
  Automatically parses options to linked variables
  option_parser_register(opp, …) link options to variables
See gpgpu_sim_config::reg_options() in gpu-sim.cc for examples

## Slide 70: Session Summary
Software Organization of GPGPU-Sim
  Interface to CUDA/OpenCL Application
  PTX Functional Simulation
  Timing Model
  Power Model: GPUWattch (Next Session)

## Slide 71: Overview
1 | Brief Background on GPU Computing | 40mins
2 | GPGPU-Sim Overview | 30mins
3 | Demo 1: Setup and Run | 15mins
Coffee Break (10:00 – 10:30am) |  | 
4 | Microarchitecture Timing Model | 85mins
Lunch (12:00 – 1:00pm) |  | 
5a | Software Organization | 25mins
5b | Timing Model (Software) | 50mins
5c | Power Model: GPUWattch | 45mins
Coffee Break (3:00 – 3:30pm) |  | 
6 | The GPU Design Space | 10mins
7a | Demo 2: Debugging Tool | 15mins
7b | Demo 3: Visualizing Performance | 30mins
8 | Extending GPGPU-Sim (with GPUWattch) | 30mins
9 | Wrap Up and Discussion | 15mins