## Slide 1: Overview
1 | Brief Background on GPU Computing | 40mins
2 | GPGPU-Sim Overview | 30mins
3 | Demo 1: Setup and Run | 15mins
Coffee Break (10:00 – 10:30am) |  | 
4 | Microarchitecture Timing Model | 85mins
Lunch (12:00 – 1:00pm) |  | 
5a | Software Organization | 25mins
5b | Timing Model (Software) | 50mins
5c | Power Model: GPUWattch | 45mins
Coffee Break (3:00 – 3:30pm) |  | 
6 | The GPU Design Space | 10mins
7a | Demo 2: Debugging Tool | 15mins
7b | Demo 3: Visualizing Performance | 30mins
8 | Extending GPGPU-Sim (with GPUWattch) | 30mins
9 | Wrap Up and Discussion | 15mins

## Slide 2: Outline
GPUWattch accuracy
Modeling
  Bottom up: McPAT
  Top down: Microbenchmarking
Using GPUWattch
Modifying GPUWattch

## Slide 3: Session Objective
After this session, you will be able to:
  Summarize what GPUWattch simulates and its accuracy with real hardware
  Describe the organization/structure of GPUWattch and how it interfaces with GPGPU-Sim
  Summarize how to include GPUWattch in your simulation and view/understand the output
  Modify GPUWattch

## Slide 4: Motivation
Performance per watt?
  Important metric to manufacturers (NVIDIA keynotes at ISCA-2010, MICRO-2011)
GPGPU research should focus on both performance and energy optimizations
The GPGPU research community is missing a configurable, cycle accurate, and validated power simulator.

## Slide 5: Power Model: GPUWattch
GPGPU-Sim introduces such a power model
  Cycle-accurate: Integrates GPGPU-Sim v3.1.2 with McPAT v0.8
  Configurable: GPGPU-Sim/McPAT configuration files
  Fine-grained: Performance/event counter driven. McPAT: Circuit level implementation
  Extensible: Can model new components or add more fine-grained per-component metrics
  Validated: Rigorously validated against NVIDIA GTX480 and Quadro Fx 5600 GPUs
Enables the exploration of new energy-efficiency optimizations for GPGPU research

## Slide 6: Contributors
GPGPU-Sim
Tor Aamodt’s research group.
McPAT
Li, S., Ahn, J. H., Strong, R. D., Brockman, J. B., Tullsen, D. M., and Jouppi, N. P. Mc- PAT: an integrated power, area, and timing modeling framework for multicore and manycore architectures. In Proceedings of the 42nd Annual IEEE/ACM International Symposium on Microarchitecture (2009) pp. 469-480.
GPUWattch
  Jingwen Leng, Ahmed ElTantawy, Tayler Hetherington, Syed Gilani, Nam Sung Kim, Tor M. Aamodt, Vijay Reddi.

## Slide 7: Measurement Setup
Hardware setup

## Slide 8: Measurement Setup
Hardware setup

## Slide 9: Accuracy Average Power
Chart: NVIDIA GTX 480

## Slide 10: Accuracy Average Power Breakdown
Chart: NVIDIA GTX 480
| LIB_K1 | LIB_K1 | MGST_K4 | MGST_K4 | HOTSP_K1 | HOTSP_K1 | memaddtwo | memaddtwo | CFD_K6 | CFD_K6 | MGST_K1 | MGST_K1 | MGST_K5 | MGST_K5 | CFD_K1 | CFD_K1 | CFD_K5 | CFD_K5 | dotproduct | dotproduct | CFD_K3 | CFD_K3 | LIB_K2 | LIB_K2 | LKYT_K1 | LKYT_K1 | LKYT_K2 | LKYT_K2 | STMCL_K1 | STMCL_K1 | HRTWL_K2 | HRTWL_K2 | KMN_K2 | KMN_K2 | memadd | memadd | memmultiply | memmultiply | KMN_K1 | KMN_K1 | MGST_K2 | MGST_K2 | CFD_K4 | CFD_K4 | MGST_K14 | MGST_K14 | MUM_K1 | MUM_K1 | MGST_K16 | MGST_K16 | Average | Average
Const | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64
HW | 138.2434 | 146.3437 | 131.6518 | 168.2948 | 155.1536 | 116.0776 | 143.4513 | 155.1986 | 173.7542 | 162.2228 | 155.9278 | 141.1398 | 192.6513 | 144.2792 | 143.3229 | 150.7066 | 163.9827 | 165.388 | 169.6634 | 156.7053 | 132.0759 | 175.4901 | 139.1454 | 150.728 | 122.1983 | 151.7519
idle_core | 1.368 | 0.73214 | 0.070143 | 0 | 0.0096259 | 9.4576 | 0.044433 | 0.0032231 | 0.0088958 | 0 | 0.0053419 | 2.0946 | 1.1934 | 1.2267 | 0.63649 | 3.3684 | 0.42544 | 0 | 0 | 0.73385 | 0.32287 | 0.0083373 | 0.57357 | 1.9833 | 11.1338 | 1.416
I-Cahce | 2.3689 | 0.10525 | 6.6226 | 8.0647 | 0.99495 | 1.9215 | 0.86606 | 1.0686 | 2.8069 | 8.1496 | 1.0686 | 1.8263 | 6.2011 | 8.0471 | 1.3485 | 4.9019 | 4.0419 | 7.8122 | 8.154 | 0.087333 | 3.6739 | 3.1821 | 1.0227 | 1.5737 | 0.87066 | 3.4712
D-Cache | 4.1229 | 6.8474 | 1 | 15.3202 | 5.2517 | 0.46726 | 3.4047 | 7.5535 | 4.2843 | 16.7737 | 7.5551 | 4.7076 | 0.014654 | 0.76259 | 1.9696 | 8.0229 | 0.099979 | 12.0603 | 12.5882 | 3.1097 | 1.4447 | 4.0678 | 8.0895 | 8.4284 | 9.7963 | 5.9097
T-Cache | 0 | 0 | 0 | 0 | 0 | 0 | 0.99978 | 0 | 0 | 0 | 0 | 0 | 9.0442 | 6.2843 | 0 | 0 | 4.992 | 0 | 0 | 0 | 38.8203 | 0 | 4.7458 | 1.3288 | 4.3299 | 2.8218
C-Cache | 1.3182 | 0 | 0 | 0 | 0 | 0 | 0 | 1.3469 | 0 | 0 | 1.3463 | 0.46467 | 0 | 2.8799 | 0 | 0.31564 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00023191 | 0.10881 | 0.00017479 | 0.31123
Shared | 0 | 0.23758 | 6.4291 | 0 | 0 | 8.4936 | 0 | 0 | 0.090581 | 0 | 0 | 0 | 1.7349 | 2.4279 | 0.092037 | 0.0019975 | 0.10582 | 0 | 0 | 0.0028399 | 4.5192 | 0 | 0.00050772 | 0 | 0.00020391 | 0.96545
Reg | 4.5827 | 0.20057 | 11.9957 | 16.1683 | 2.1454 | 3.4366 | 1.8056 | 1.809 | 5.2244 | 15.937 | 1.8094 | 3.6068 | 14.3967 | 14.3108 | 2.6647 | 8.7242 | 7.8406 | 15.6136 | 16.2428 | 0.32774 | 8.2944 | 6.5861 | 2.0514 | 2.2213 | 1.7597 | 6.7902
Exe | 26.5755 | 0.32839 | 25.3596 | 22.5258 | 4.9404 | 10.4606 | 3.3898 | 3.6794 | 20.7025 | 24.2036 | 3.6802 | 17.8464 | 43.0798 | 29.3049 | 3.4247 | 17.053 | 13.666 | 25.0925 | 28.6225 | 0.23836 | 12.3513 | 57.058 | 2.494 | 3.2589 | 1.9439 | 16.0512
DRAM | 23.4246 | 59.1248 | 0.33889 | 0.42646 | 65.4914 | 10.747 | 55.4595 | 52.2079 | 54.5369 | 0.45224 | 52.213 | 47.0067 | 0.13625 | 0.30378 | 53.9606 | 10.5302 | 83.0556 | 0.35975 | 0.35847 | 63.9117 | 14.3627 | 63.9921 | 51.4323 | 16.9467 | 30.7201 | 32.46
L2-Cache | 7.3286 | 11.1092 | 5.2774 | 26.7027 | 6.3722 | 0.13087 | 5.7868 | 12.8294 | 7.7853 | 12.7042 | 12.8318 | 6.3794 | 32.0287 | 18.6773 | 1.4121 | 10.2506 | 0.17215 | 9.5272 | 7.289 | 2.7509 | 2.1479 | 3.3056 | 31.651 | 18.24 | 27.206 | 11.1959

## Slide 11: Accuracy Dynamic Traces

## Slide 12: McPAT
McPAT essentially boils down to a linear equation
N = # of components modelled
αi = Activity for component i
= Peak power for component i
= Power consumption for idle SM

## Slide 13: GPUWattch Structure GPGPU-Sim with McPAT
Modified McPAT
Modifications: Specific micro-architectural components
GPGPU-Sim
Modifications: Add required performance counters
A Comprehensive Framework for Performance and Energy Optimization Research
Interface
Interface
Static Power
Dynamic Power
Detailed Power Stats
Detailed Performance Stats
Feedback-driven Optimizations
Performance counters

## Slide 14: Modeling GPGPU-Sim with McPAT
Inevitable modeling uncertainties of components
  Unknown size or configuration
  Unknown existence of components
Results in a 2 stage modeling process
  Stage 1: Bottom up
    Model GPGPU components in McPAT to build the initial power model
    Identify Inaccuracies in the initial model
  Stage 2: Top down
    Resolve the inaccuracies using strategically designed microbenchmarks
    Refine the initial power model

## Slide 15: Modeling Bottom Up: McPAT Modifications
Baseline McPAT
  Multi-core CPU power simulator
  Detailed models for CPU microarchitectural blocks
Modified McPAT to account for GPU specific microarchitectural components
Some of the main components that were added/modified:
  SM Pipeline
  Register File
  Caches
  Shared Memory
  Execution Units
  Main Memory

## Slide 16: Modeling Bottom Up: McPAT Modifications
SM Pipeline
  In-order, multithreaded SIMD pipelines
  Shared: E.g, scheduler, instruction fetch/decode, reg. file
  Separate: E.g., functional units
Register Files
  Banks (16, dual port): 1kb wide, 64-entry SRAM
  Operand collection Network: 1kb wide, 16X16 crossbar
  Operand collectors: 1kb wide SRAM

## Slide 17: Modeling Bottom Up: McPAT Modifications
Caches
  L1, L2, Texture, Constant cache: Architecture dependent sizes
  Memory-coalescing logic: Synthesis based
Shared Memory
  Banks (32): Architecture dependent sizes
  Network: 32 x 32 crossbar network
Notes: Shared Memory: Heavily multi-banked. Doesn’t have tagging structures as normal caches

## Slide 18: Modeling Bottom Up: McPAT Modifications
Execution units
  Integer ALUs: Synthesis-based
  Floating point unit: Synthesis-based
  Special-function unit: Synthesis-based
Main memory
  Memory controller: McPAT model
  NoC: McPAT model
  GDDR5/GDDR3: Empirical model
Notes: Memory controller: Changed data rates to have higher throughput, high bandwidth. No changes to architecture

## Slide 19: Modeling Bottom Up: GPGPU-Sim modifications
Added performance counters required by McPAT
Structures added to manage performance counters
Files added to interface with McPAT
Existing timing model not affected by any GPGPU-Sim modifications

## Slide 20: Modeling Bottom Up: GPGPU-Sim modifications
Main Component | Performance Counters | Main Component | Performance Counters
Instruction cache | Read hit | L2 Data cache | Read hit
 | Read miss |  | Read miss
L1 Data cache | Read hit |  | Write hit
 | Read miss |  | Write miss
 | Write hit | Memory | Reads
 | Write miss |  | Writes
Texture cache | Read hit |  | Precharges
 | Read miss | Register file | Reads
Constant cache | Read hit |  | Writes
 | Read miss |  | Non-register file operand
Current version utilizes 30 performance counters

## Slide 21: Modeling Bottom Up: GPGPU-Sim modifications
Main Component | Performance Counters | Main Component | Performance Counters
Decoding/Scheduling | Total # instructions | Shared Memory | Accesses
 | FP_INT instructions |  | 
Pipeline dutycycle | Fraction of committed instructions per cycle | Execution Units | SP accesses
Idle core | Number of cycles each SM is idle |  | SFU accesses
Interconnect | # of flits from SIMT cores to Memory Partition |  | 
 |  |  | FPU accesses
 | # of flits from Memory Partition to SIMT cores |  | 
Current version utilizes 30 performance counters

## Slide 22: Modeling Top Down: Refinement
Why Refinement?
  Modeling uncertainties
  Adjust hardware assumptions
  Account for black boxes (Unknown unknowns)
How?
  Microbenchmarking
Example: Texture cache
  Model: Regular cache
  Reality: Additional functions
    Address translations, reorder buffers to decouple tags from data, texture samplers, etc.
  These are treated as black boxes and accounted for in the refinement process

## Slide 23: Using GPUWattch Configuration Options
GPGPU-Sim: gpgpusim.config
  -power_simulation_enabled (1/0)
  -mcpat_xml_file <filename>.xml
McPAT configurations: <filename>.xml
  Default: mcpat.xml
  Currently, must be included in working directory

## Slide 24: Using GPUWattch Understanding Simulation Output
-power_simulation_enabled 1
  gpgpusim_power_report_(date&time).log
    Contains avg/max/min total powers and their power breakdowns for each component per kernel.
-power_trace_enabled 1
  gpgpusim_power_trace_(date&time).log.gz
    Contains detailed avg power breakdown (CSV)
  gpgpusim_metric_trace_(date&time).log.gz
    Contains detailed performance counter trace (CSV)

## Slide 25: Using GPUWattch Advanced: For your research
Start
Set initial Configurations
Extending?
Missing Components?
Regular Structure
- Model performance impact
- Instantiate a new component from existing classes
-Model performance impact
- HDL Synthesis
- Generate corresponding performance counters
- Pass them to McPAT
Compile & Run
Simulation ….
Yes
No
No
Yes

## Slide 26: Using GPUWattch Software organization
GPGPU-Sim (<root>/src/gpu-sim/)
power_stat.cc/h
power_interface.cc/h
McPAT (<root>/src/mcpat/)
gpgpu_sim_wrapper.cc/h
gpgpu_sim.verify
Modified McPAT
gpgpu_sim.verify
GPGPU-Sim
power_stat
gpgpu_sim_wrapper
power_interface
Performance counters
Dynamic/Static power Runtime feedback stats

## Slide 27: Using GPUWattch Adding a new component
XML File
mcpat.xml
Static Configuration
XML Parser
XML_parse.cc
McPAT Parser
Interface
Class root_system
(XML_parse.h)
McPAT’s internal
Representation of XML File
Step 1: If necessary, add new configuration option
Notes: *This step is optional. It is only necessary when the parameters of
this component can not be decided using other existing components.

## Slide 28: Using GPUWattch Adding a new component
Step 2
  Decide whether this component is already modeled in McPAT
    E.g., McPAT already provides models for DataCache (array.h), and FunctionalUnit (logic.h)
  If not modeled in McPAT, we need to use the basic structures provided by CACTI to model the component or synthesize the component manually.

## Slide 29: Using GPUWattch Example: Adding constant cache
Step 1: Change the XML file, and the corresponding class in XML_parse.h (class system_core for constant cache)
Struct dcache_systemcore holds all cache parameters specified in the XML file.
Cache parameters

## Slide 30: Using GPUWattch Example: Adding constant cache
Step 2:
  Add the component in the LoadStoreU class (core.h)
  Modify the constructor and compute function in LoadStoreU class (core.cc)
ccache.caches = new ArrayST(&interface_ip, "ccache", Core_device,
coredynp.opt_local, coredynp.core_ty);

## Slide 31: Using GPUWattch Example: Adding the Memory Coalesce Logic
Change corresponding XML file and object
There are three array structures for the MCL
    Pending Request Table (PRT)
    Pending Request Count (PRC)
    Thread Masks

## Slide 32: Using GPUWattch Example: Adding the Memory Coalesce Logic
Use the CACTI interface to construct these arrays
PRT (memoryctrl.cc)
  Per row data size = 64 Bytes
  Warp ID (6 bits) | Memory address (32 bits) per thread | Request Size (2-bits) per thread |
6 bits | 32 x 16 bits | 2 x 16 bits
Notes: the physical implementation of SRAM will be optimized by McPAT by using the EDP metric

## Slide 33: Using GPUWattch Example: Adding Synthesized Model
Describe the hardware in Verilog HDL
Synthesize it using DesignVisionTM
  40nm TSMC® standard cell technology library
  Timing constraints according to the GPU clock
Annotate switching activity
  Use a representative set of inputs to test the synthesized design
  Dump the activity factors for all the cells used in the design

## Slide 34: Using GPUWattch Example: Adding Synthesized Model
Use PowerCompilerTM to annotate all the cells with switching activity information
Dynamic and leakage power reports are generated from PowerCompilerTM

## Slide 35: Using GPUWattch Example: Adding Synthesized Model
Incorporate the power numbers in McPAT
  McPAT model may use a different technology library/Vdd
  Scale the power numbers according to McPAT’s internal scaling models
Notes: 90 = 90nm technology library.
It is the 90nm tech library. This is how McPAT internally scales power numbers

## Slide 36: Summary
GPGPU-Sim power model: GPUWattch
  Accuracy
  How it’s modeled
    GPGPU-Sim
    McPAT
  How to enable
  Software organization
  How to modify

## Slide 37: Overview
1 | Brief Background on GPU Computing | 40mins
2 | GPGPU-Sim Overview | 30mins
3 | Demo 1: Setup and Run | 15mins
Coffee Break (10:00 – 10:30am) |  | 
4 | Microarchitecture Timing Model | 85mins
Lunch (12:00 – 1:00pm) |  | 
5a | Software Organization | 25mins
5b | Timing Model (Software) | 50mins
5c | Power Model: GPUWattch | 45mins
Coffee Break (3:00 – 3:30pm) |  | 
6 | The GPU Design Space | 10mins
7a | Demo 2: Debugging Tool | 15mins
7b | Demo 3: Visualizing Performance | 30mins
8 | Extending GPGPU-Sim (with GPUWattch) | 30mins
9 | Wrap Up and Discussion | 15mins